## Slide 1: Speculative Return Address Stack Management Revisited

## Slide 2: Paper Intro
ACM Transactions on Architecture and Code Optimization (TACO)
  Volume 5 Issue 3, Nov 2008
Author:
  Hans Vandierendonck Ghent University, Gent, Belgium
  André Seznec IRISA/INRIA, Cedex, France

## Slide 3: Contents
RAS Intro
  Big Picture of RAS
  Abstract on Paper
  Introduction on Paper
Detecting Overflows and Wrong-Path on Conventional RAS
  Simple RAS PUSH
  Simple RAS POP
  Simple RAS with CD-TOS
  CT-RAS Recovery
SC-RAS and Reallocation Detecting
  SD-RAS PUSH
  SD-RAS POP
  SD-RAS Advantage
  SD-RAS Disadvantage
  SD-RAS with Empty bit
  SD-RAS with MAX
Evaluation on Paper

## Slide 4: Big Picture of RAS
+
4
PC
Push
Return
Address
BTB
RETURN?
Pop
Return
Address
Predicted next PC
TOS

## Slide 5: Abstract on Paper
Present two low-cost corruption detectors for RAS.
They detect RAS overflows and wrong-path corruption.
When corruption is detected, BTB can be used as a free backup predictor.

## Slide 6: Introduction on Paper
The RAS is typically implemented as a circular buffer to store return addresses and a top-of-stack pointer (TOS) pointing to the current top of the stack.
The RAS must be updated for speculatively fetched instructions.
When a misprediction is detected, the call instruction may be squashed, leaving the wrong return target on the RAS.

## Slide 7: Simple RAS PUSH
TOS
TOS
TOS
TOS
TOS
RAS Overflow

## Slide 8: Simple RAS POP
TOS
RAS Underflow
TOS
TOS
TOS
TOS

## Slide 9: Simple RAS with CD-TOS
TOS
TOS
TOS
TOS
CD-TOS
CD-TOS
CD-TOS
CD-TOS
FW=0
FW=0
FW=0
FW=0
Detect RAS overflows by means of a second pointer to the RAS (Corruption Detection TOS) and FW (First Wrap bit).

## Slide 10: Simple RAS with CD-TOS
TOS
TOS
RAS Overflow
CD-TOS
CD-TOS
FW=0
FW=1
When FW=1, CD-TOS==TOS Overflow.
When RAS overflow occurs, CD-TOS is incremented by 1.

## Slide 11: Simple RAS with CD-TOS
TOS
TOS
TOS
TOS
CD-TOS
CD-TOS
CD-TOS
CD-TOS
FW=1
FW=1
FW=1
FW=1

## Slide 12: Simple RAS with CD-TOS
TOS
CD-TOS
RAS Underflow
TOS
FW=1
FW=0
When RAS underflow occurs, CD-TOS is decremented by 1.
CD-TOS

## Slide 13: CT-RAS Recovery
Wrong Path
ORed
Simple RAS with extra local check point mechanism(CheckTOS).
  Every entry in the RAS is augmented with a corruption bit.
  When Corruption is detected, every bits between Current CTOS (CTOSc) and Recover CTOS (CTOSr) is Ored.
  The ORed value (corrupt Vector) will be updated to every corruption bits.

## Slide 14: SD-RAS PUSH
TOS
TOS
TOS
TOS
NEXT
NEXT
NEXT
NEXT
Self Detection RAS is proposed by Jourdan et al.
The SC-RAS explicitly links each RAS entry to the logically lower RAS entry using a next-on-stack (NOS).
The next entry to allocate is indicated by the NEXT pointer.

## Slide 15: SD-RAS POP
TOS
NEXT
By tracking the NOS, SC-RAS Pops its Prediction.
When RAS Pop, NEXT will be not decremented.

## Slide 16: SD-RAS Advantage
Call
Conditional Call (Predict miss)
Return
Return
Call
(Detect Predict miss)
Return
TOS
TOS
TOS
TOS
TOS
Recovery But miss Predict
TOS
Wrong path Corruption is not covered in Simple RAS.
When a misprediction is detected, the call instruction may be squashed, leaving the wrong return target on the RAS.

## Slide 17: SD-RAS Advantage
TOS
TOS
TOS
TOS
TOS
NEXT
NEXT
NEXT
NEXT
Call
Conditional Call (Predict miss)
Return
Return
Call
(Detect Predict miss)
Return
NEXT
TOS
NEXT
Wrong path Corruption is covered in SD-RAS.
The Correct Path is leaved in the SD-RAS when Recovering.

## Slide 18: SD-RAS Disadvantage
TOS
TOS
TOS
TOS
NEXT
NEXT
NEXT
NEXT
Call
Return
Call
Return
Call
Return
If same function called repeatedly, SD-RAS can be overwritten with the same value.
  SD-RAS can be overflowed more frequently.

## Slide 19: SD-RAS With Empty bit
TOS
NEXT
E=1
Empty bit
E=0
TOS
NEXT
To support the corruption detector, empty bit to the SC-RAS is added.
  Initially set to 1.
  When Pushed, set to 0.

## Slide 20: SD-RAS With Empty bit
TOS
NEXT
E=0
TOS
NEXT
E=0
TOS
NEXT
E=0
TOS
NEXT
E=0
TOS
NEXT
E=1
  When RAS Pop and no more valid entry, set to 1.
When empty bit is set, the RAS is not popped since there are no more valid entries in the RAS.

## Slide 21: SD-RAS with MAX
TOS
TOS
TOS
TOS
TOS
NEXT, MAX
NEXT, MAX
NEXT, MAX
NEXT, MAX
Call
Conditional Call (Predict miss)
Return
Return
Call
(Detect Predict miss)
Return
NEXT, MAX
TOS
NEXT
MAX
The NEXT pointer is recovered from checkpoint storage when detecting a misprediction, so the corruption of these entries can not be deduced from the stack pointers (Add a MAX pointer).
MAX tracks the maximum value of the NEXT pointer.
Valid [MAX-N, NEXT]

## Slide 22: Evaluation on Paper
The SC-RAS only suffers from overflow mispredictions.
Simple RAS and CT-RAS are suffer from wrong-path and overflows.
When RAS size is small(4~) CT-RAS is the most effective design.
  SC-RAS is not effective because of RAS Overflow.
When RAS size is big (~128) SC-RAS design is the most effective design.
  Because of wrong-path recovery, SC-RAS can be powerful.

## Slide 23: The End