## Slide 1
Lecture 3. RAS Issues in Lucida
Prof. Taeweon Suh
Computer Science Education
Korea University
COM609 Topics in Embedded Systems

## Slide 2: Return Address Stack Issues in Lucida
Push and Pop timing
  Push the return address in ID stage?
    What if the conditional branch turns out to be predicted wrong? Corrupt RAS
  Pop from RAS in IF stage?
    Need to decode the return instruction in IF stage: JPLR (Jump to Link Register), POP PC, JR?
Unmatched call/return sequences
  What if the conditional branch turns out to be predicted wrong?
    Corrupt RAS
  Exception or Interrupt
    What is the instruction for returning from interrupt? (SR restore)
  Context Switch
    Timer interrupt
  Clear RAS at the reception of interrupt or exception?
  longjmp() / setjump()?
Misprediction detection and correction logic

## Slide 3: Basic Operation in Lucida
8-entry RAS?
RAS reset conditions,
  Overflow/Underflow
  Unmatched sequence
Or use circular buffer and let it overflow or underflow? If the RAS return is wrong, then reset the RAS..

## Slide 4: RAS Corruption due to Conditional Branch Misprediction
No corruption because the conditional branch is resolved in ID stage
  If the speculated instruction is jlr-kind instruction, it will be squashed immediately because it is in IF stage, assuming that jlr-kind inst. pushes the return address in ID stage

## Slide 5: RAS Corruption due to RAS Misprediction
It could come from unmatched sequence
(jal, jalr) – (jplr, jr?) pair
  We don’t consider jr
  jplr is resolved in ID stage. No problem in case of the misprediction. The same reason as the conditional branch misprediction
pop pc is resolved in MEM stage. Then, what if the prediction was wrong? There are 3 instructions in the pipe after POP PC
  We almost decided to use the normal stack-like structure (not the one in Patt’s paper)
  Checkpoint TOS and NEXT (Patt’s paper) at each prediction with RAS? Need at most 2-3 buffers
RAS reset conditions?

## Slide 6: Misc
We don’t take the following cases into account in RTL design since it would occur extremely rarely (Make common cases faster!)
  JAL, JPLR: immediately return from subroutine
    It could corrupt the instruction queue since RAS push from JAL occurs in ID stage? Then IQ could be filled with instructions from wrong path? I am not quite sure…

## Slide 7: Nelahem Case Study
16-entry Return Stack Buffer

## Slide 8: General Lucida Questions
What happens in IF stage when the conditional branch is turned out to be mis-predicted?
When executing jal, jalr instructions, the return address is saved in ID stage?